## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID -
Problem Statement Title - AI-Powered Camera-Free Smart Pen for Handwriting Digitization
Theme -
PS Category – Software + Hardware
Team ID -
Team Name -

## Slide 2: IDEA TITLE
Proposed Solution :
• AI-powered smart pen that digitizes handwriting written on ordinary paper without using a camera or special paper.
• Uses IMU, pressure sensor, ESP32-C3 and Bluetooth Low Energy (BLE) to capture pen movement, writing pressure and stroke patterns in real time.
• Applies signal processing, sensor fusion and machine learning to reconstruct pen trajectories and recognize handwritten characters/strokes.
• Converts handwritten content into digital handwriting/text on a laptop or smartphone and can support features such as digital notes and signature verification.
• Unique feature: combines compact embedded sensing, AI-based trajectory analysis and wireless communication to create a low-cost camera-free handwriting digitization system using regular paper.

## Slide 3: TECHNICAL APPROACH
Technologies :
• Hardware: ESP32-C3-MINI-1, MPU6050/6-axis IMU, force-sensitive resistor (FSR), Li-Po battery, charging module and custom PCB.
• AI/Software: Python, NumPy, SciPy, Scikit-learn/PyTorch, signal processing, sensor fusion and machine learning.
• Communication: Bluetooth Low Energy (BLE) for real-time transfer of pen sensor data to a laptop/mobile device.
• Application: Python/Streamlit-based interface for live handwriting reconstruction, digital note generation and signature analysis.
Implementation Flow :
Pen Movement & Pressure → IMU/FSR Sensing → ESP32-C3 Data Acquisition → Calibration & Noise Filtering → Sensor Fusion & Feature Extraction → AI-Based Stroke/Trajectory Reconstruction → BLE Transmission → Digital Handwriting / Text Output
❖ AI Approach :
Sensor Data → Pre-processing → ML Model → Stroke/Character Recognition → Digital Reconstruction

## Slide 4: FEASIBILITY AND VIABILITY
• Uses low-cost, compact and commercially available components such as ESP32-C3, IMU and pressure sensors, keeping the prototype within the ₹5,000–₹8,000 budget.
• Compact and lightweight design can be developed using a custom PCB, making the system practical for integration into a pen-like enclosure.
• Handwriting and sensor datasets can be collected directly from multiple users and used to train and evaluate machine-learning models.
• BLE-based communication and local processing enable real-time data transfer with low power consumption and reduce dependence on internet connectivity.
• Challenges: IMU drift, writing-style variation, limited battery capacity, sensor noise, compact PCB design and accurate trajectory reconstruction.
• Solutions: sensor calibration, filtering and sensor fusion, user-diverse training data, lightweight ML models, optimized power management and progressive miniaturization.

## Slide 5: IMPACT AND BENEFITS
Reduces response time during accidents and emergencies.
Provides real-time worker location and safety status.
Helps detect hazardous gases and environmental conditions before they become critical.
Reduces the risk of undetected falls, injuries and prolonged exposure to hazards.
Improves workplace safety and enables data-driven safety management.
Can reduce accident-related medical, operational and financial losses.
Suitable for construction sites, mines, tunnels and other high-risk workplaces.

## Slide 6: RESEARCH AND REFERENCES
Research papers on :
IMU-based handwriting recognition using sensor-equipped pens
Handwriting trajectory reconstruction from inertial sensor data
Sensor fusion using IMU and force/pressure sensing for smart pens
Writer-independent handwriting recognition using machine learning and deep learning
• ESP32-C3-MINI-1 Technical Documentation — Espressif Systems
• Bluetooth Low Energy Documentation — Espressif Systems
• MPU6050 / Inertial Sensor Technical Documentation — TDK InvenSense
• Force Sensing Resistor (FSR) Datasheet — Interlink Electronics
• OnHW Dataset: Online Handwriting Recognition from IMU-Enhanced Pens — ACM
• Surface-Free Multi-Stroke Trajectory Reconstruction Using an IMU-Enhanced Digital Pen
• Robust and Efficient Writer-Independent IMU-Based Handwriting Recognition — 2026